## Slide 1: A Perspective on Facilitated Access to Custom IC Design in Leading-Edge CMOS Technology
Linton G. Salmon
EDA for HPC, Cloud and Server SoC Design Workshop
June 7, 2015
Approved for Public Release, Distribution Unlimited

## Slide 2: Performance versus Development Cycle Times
 | Qty | Power Req. | Dev. Cycle Time | Current Character
General Purpose Central Processor (CPU) | 28 | 1260W | ~6 months | Low performance at power Flexible Quick to implement
Field Programmable Gate Array (FPGA) | 4 | 120W | ~12 months | Low performance at power Flexible Moderately quick to implement
Custom Integrated Circuit (Custom IC) | 1 | 5W | ~24 months | High performance at power Relatively inflexible Slow to implement
Today you have to choose between performance and schedule/cost.
Example Data from representative DoD design
Approved for Public Release, Distribution Unlimited

## Slide 3: Performance versus Development Cycle Times
We need to change the design environment so we can have BOTH
We need to enable fast, flexible, and high performance custom ICs, bringing DoD system components up to speed with commercial technology and practices, but at a fraction of the effort even at the expense of increased area.
Approved for Public Release, Distribution Unlimited

## Slide 4: Commercial and DoD Access to Leading-Edge CMOS Technology
Commercial
Most volume at 28nm
Leading-edge products shipped at 20nm
Pilot production at 14nm
  Driven by large companies
  PDK widely available 2Q14
All leading-edge processes bulk
Leading-Edge technology available at multiple facilities
Turnaround time: 2-4 months (28nm)
DoD
Most volume at ≥ 130nm
Leading-edge products shipped at 90nm
Pilot production at 45nm
  Driven by availability of infrastructure
  ~ 3 nodes behind 14nm
All leading-edge processes SOI
Leading-Edge technology confined to one at-risk facility, IBM–East Fishkill
Turnaround time: 9-12 months (32nm)
Current Status
Need
Regular, dependable, fast leading-edge CMOS multiple-project runs for DoD
Full, supported commercial design enablement from foundry
Facilitated commercial component circuit (IP) access
A common methodology for DoD-specific IP generation/distribution
Greatly improved design methodology to sharply reduce design time/effort
Approved for Public Release, Distribution Unlimited

## Slide 5: Why Use Leading Edge CMOS Custom Integrated Circuits?
Chart: Technology Node
| 1.0 | 1.0 | 1.0 | 1.0 | 1.0 | 1.0 | 1.0 | 2.0 | 2.0 | 3.0 | 3.0 | 3.0 | 3.0 | 3.0 | 4.0 | 4.0 | 4.0 | 4.0 | 4.0 | 4.0 | 4.0 | 4.0 | 4.0 | 5.0 | 5.0 | 5.0 | 5.0 | 5.0 | 5.0 | 5.0 | 5.0 | 5.0 | 5.0 | 6.0 | 7.0 | 7.0 | 8.0 | 7.0 | 7.0 | 8.0
GOPS/W | 298.5383 | 133.3521 | 668.3439 | 562.3413 | 562.3413 | 5.9566 | 1000 | 211.3489 | 0.453 | 2.8184 | 8.9125 | 1.064 | 1000 | 411.3 | 564 | 0.4217 | 0.79433 | 1.9953 | 14.1254 | 5.6234 | 28.1838 | 3.2 | 1.2 | 35.2 | 14.2 | 3.7584 | 8.9125 | 2.5119 | 340 | 2215 | 18.73 | 23.04 | 50 | 3.1623 | 240 | 1408 | 2500 | 2400 | 14075 | 25000
10x – 1000x
General Purpose
GPU
General Process
CPU
FPGA
Custom IC
GP GPU
GP CPU
Intel CPU
Custom
IC
130nm 90nm 65nm 40/45nm 28/32nm 20/22nm 14/16nm 10nm
5x – 10X
Data from ISSCC papers 2010 – 2013
and "Energy Efficient Computing on Embedded and Mobile Devices” on nVidia.com
Approved for Public Release, Distribution Unlimited

## Slide 6: Current Design Flow Takes so Long that it is Throttling DoD Access to Advanced Technology
Chart: Number of Weeks
| Current DoD CIC Design Flow | Commercial CIC Design Flow | Novel Design 10X
RTL Design and Synthesis | 16.5455 | 6.7879 | 3.3091
Design for Test | 10 | 4.1026 | 2
Verification and physical design | 51.4545 | 21.1096 | 10.2909
Manufacturing | 52 | 7 | 14
TODAY
Design effort model derived from commercial and DoD sources
Existing DoD custom IC product cycle time can take as long as 2.5 years.
  60%: Design (most of which is verification)
  40%: Fabrication (20%/fab spin)
DESIGN
PORT/ MIGRATE
REPOSITORY
DoD Commercial
28nm node example
130 Weeks
10 person team
~ 0.1B transistors
39 Weeks
400 person team
~ 6.8B transistors
Fabrication
NRE
Design
NRE
Verification
Design
Fab
#1
Fab
#2
Notes: CRAFT will solve the problem directly by reducing the amount of effort required to design a custom IC. The reduction will be achieved through leveraging modern programming techniques to the design process and by improving use of hierarchy to simplify design and reduce required verification.

## Slide 7: Current Design Flow Takes so Long that it is Throttling DoD Access to Advanced Technology
Chart: Number of Weeks
| Current DoD CIC Design Flow | Commercial CIC Design Flow | Novel Design 10X
RTL Design and Synthesis | 16.5455 | 6.7879 | 3.3091
Design for Test | 10 | 4.1026 | 2
Verification and physical design | 51.4545 | 21.1096 | 10.2909
Manufacturing | 52 | 7 | 14
Future
TODAY
Design effort model derived from commercial and DoD sources
Existing DoD custom IC product cycle time can take as long as 2.5 years.
  60%: Design (most of which is verification)
  40%: Fabrication (20%/fab spin)
Using “Object Oriented Design” and enhanced hierarchy, we want to achieve:
  Reduction in design time by 10X through a strong reduction in verification time and removal of minimum area constraint
  “First Time Right” design methods to eliminate the need for repeated fabrication runs.
  Reduction in fabrication time to 2X commercial
DoD Commercial Need
28nm node example
130 Weeks
10 person team
~ 0.1B transistors
39 Weeks
400 person team
~ 6.8B transistors
Fabrication
NRE
Design
NRE
30 Weeks
10 person team
~ 0.2B transistors
Verification
Design
Fab
#1
Fab
#2
Data from plenary talk DAC–2013 by Ivo Bolsens (Xilinx)
and conversations with DoD contractors
Approved for Public Release, Distribution Unlimited

## Slide 8: 14nm is the Most Fabrication Cost-Effective Node for DoD
Chart: CMOS Process Node
| 90nm | 65nm | 40nm | 28nm | 14nm
Mask Cost (k$) | 500 | 670 | 1300 | 2500 | 5000
Set up costs (k$) | 400 | 500 | 700 | 1000 | 1000
Wafer Cost (k$) | 300 | 600 | 1000 | 1750 | 3000
Custom IC Fab NRE* Costs
Fab NRE Costs per kgate
Chart: CMOS Process Node
| 90nm | 65nm | 40nm | 28nm | 14nm
Cost/kgates (k$) | 2.4396 | 2.0669 | 1.8244 | 1.7229 | 1.6669
Chart: CMOS Process Node
| 90nm | 65nm | 40nm | 28nm | 14nm
 | 637 | 1109 | 2130 | 3946 | 6992
Gate Density
It may be counter-intuitive, but for DoD, 14nm technology fabrication is CHEAPER per gate than 28nm technology and MUCH CHEAPER than 90nm technology, while providing greatly improved performance at power!
Fab NRE – Fabrication Non Recurring Engineering
(masks, wafers, set up)
From International Business Strategies, 2013
Multi Project Wafer (MPW)
Approved for Public Release, Distribution Unlimited

## Slide 9: We Need a New Custom IC Design Flow
VHDL
Raise Level of Abstraction
Use existing EDA tools
Higher level of hierarchy
Use of generators/constructs
CELL/WIRE
OASIS
Place & Route
Layout Description
CELL/WIRE
HL Code
VERIFICATION
RTL
VERIFICATION
OASIS
SPICE
New Software Tool
Use of modern software engineering methods
Automated representation translation
Automated verification
Reduces effort required to port design to a 2nd source foundry
Distributed through a government IP repository
Object Oriented Design (OOD) Flow
High level object oriented language -> Schematic
SPICE
HL Code
OOD FLOW
Existing
ASIC
Flow
Approved for Public Release, Distribution Unlimited

## Slide 10: Only 4 Companies Provide FinFET CMOS Foundry Services
X
Approved for Public Release, Distribution Unlimited
Samsung
Intel
Global Foundries
TSMC
IBM
GlobalFoundries
TSMC
Intel
IBM
Samsung
Samsung

## Slide 11: DoD Needs a Facilitated Flow to Port/Migrate DoD Custom IC Designs
Unique to Foundry/Node
1,000,000s of elements
Logical Descript’n
Gate Level Descript’n
Place & Route
Current ASIC
Design Flow
High Level description
Schematic Descript’n
Layout Descript’n
Unique to Foundry/Node
100s of elements
Stored in gov’t repository
New
Design Flow
Place & Route
Layout Descript’n
Object Oriented Design (OOD) Flow
High level object oriented language -> Transistor
Compiled
We need to sharply reduce the amount of “foundry unique” work required for a design.
Using an OOD Flow would reduce the effort to port designs to a new foundry
and/or to migrate them to a new technology node
Approved for Public Release, Distribution Unlimited

## Slide 12: Potential Multi-Project Run Schedule
3Q15
1Q16
2Q17
3Q17
4Q17
1Q18
2Q18
3Q18
4Q18
1Q19
2Q19
3Q19
4Q19
4Q15
3Q16
2Q16
1Q17
4Q16
Release of PDK
Wafer fab and die reticulation/delivery
Approach
  16/14nm FinFET multi-project shuttle
  Design submission date is planned for February, 2016
  Cost will be approximately $50K/6mm2 project
  Turnaround time will be 6 months, GDS-In to die delivered to design teams
  Training will be provided for design teams (face-to-face and web-based)
  Aggregation and foundry-interface/design support will be provided
Wafer fab and die reticulation/delivery
Wafer fab and die reticulation/delivery
Wafer fab and die reticulation/delivery
Approved for Public Release, Distribution Unlimited

## Slide 13: Potential Shuttle Details
Process flow: FinFET process flow
  Bulk FinFET transistors with dual gate oxide
    SVT/LVT/1.8V IO transistor
  BEOL stack: 9 levels of Cu wiring compatible with fundamental IP
  Standard passive components (no deep trench capacitor)
  Standard eFuse and anti-fuse blocks
  HP SRAM bit cell
Tentative schedule
  PDK available: August, 2015
  Training: September - November, 2015
  Firm shuttle commitment from users required: November, 2015
  Design submission (GDS-In): February, 2016
  Die back to users: August, 2016 (GDS-In + 6 months)
Aggregator/interface/training organization
  All questions for the foundry will go through foundry interface
  All GDS will be sent to aggregator
User cost will be ~ $50K/(3mmX2mm) project
Approved for Public Release, Distribution Unlimited

## Slide 14: How Do I Sign Up/Ask Questions?
Indicate interest by sending an email to: caroline.rudolph.ctr@darpa.mil
Please provide the following information:
  User point of contact
  User organization
  Brief description of the purpose for the project(s)
  Associated US Government agency
  Area required (in units of 2mmX3mm blocks)
  Any questions you may have
Approved for Public Release, Distribution Unlimited

## Slide 15: DARPA Wants to “Ride the Wave” to Exciting Places!
The “Wave” (Smartphone market example)
Global consumers
> $265B market (global revenue in 2013)*
Drives leading-edge CMOS technology
Requires digital, analog, and RF advances
Burdened by large SoC design investments
Pays for large, production wafer volumes
“Generates” the power of the wave
* Statista.com website
The “Surfer” (DoD system development/deployment)
Global suppliers
< $1.5B market (US Government business in 2013)**
Utilizes commercially-driven CMOS technology
Leverages digital, analog, and RF advances
Drives new, boutique design/architecture approach
Pays for low wafer volumes
“Utilizes” the power of the wave
** IC Insights “IC Market Drivers 2014 Update”
Approved for Public Release, Distribution Unlimited
U.S. Marine Corps Photo
Frank Kovalchek from Anchorage, Alaska, USA

## Slide 16
Approved for Public Release, Distribution Unlimited