## Slide 1: SoC Design Methodology for Exascale Computing
Shekhar Borkar
Intel Corp.
June 7, 2015
This research was, in part, funded by the U.S. Government, DOE and DARPA. The views and conclusions contained in this document are those of the authors and should not be interpreted as representing the official policies, either expressed or implied, of the U.S. Government.

## Slide 2: Outline
Exascale motivation & challenges
Future Exascale straw-man system design
  Compute
  Memory
  Interconnect
Design challenges and solutions
Choice of process technology
SoC Challenges

## Slide 3: From Giga to Exa, via Tera & Peta
Chart: Relative Transistor Perf
| 1986 | 1988 | 1990 | 1992 | 1994 | 1996 | 1998 | 2000 | 2002 | 2004 | 2006 | 2008 | 2010 | 2012 | 2014 | 2016 | 2018
Freq | 1 | 1.3333 | 2.75 | 5.5 | 16.6667 | 27.75 | 50 | 83.3333 | 166.6667 | 191.6667 | 216.6667 | 250 | 275 | 302.5 | 332.75
Giga
Tera
Peta
Exa
32x from transistor
32x from parallelism
8x from transistor
128x from parallelism
1.5x from transistor
670x from parallelism
System performance from parallelism

## Slide 4: Where is the Energy Consumed?
50pJ per FLOP
50W
150W
100W
100W
600W
Decode and control
Address translations…
Power supply losses
Bloated with inefficient
architectural features
~1KW
Compute
Memory
Com
Disk
10TB disk @ 1TB/disk @10W
0.1B/FLOP @ 1.5nJ per Byte
100pJ com per FLOP
5W
2W
~5W
~3W
5W
Goal
~20W
Teraflop system today

## Slide 5: The UHPC* Challenge
20 pJ/Operation
20MW, Exa
20W, Tera
20KW, Peta
*DARPA, Ubiquitous HPC Program
20 mW, Mega
2W, 100 Giga
20 mW, Giga

## Slide 6: Top Exascale Challenges
System Power & Energy
New, efficient, memory subsystem
Extreme parallelism, data locality, gentle-slope programmability
New execution model comprehending self awareness with introspection
Resiliency to provide system reliability
System efficiency & cost

## Slide 7: Exascale HW Design Challenges
1. NTV Logic & Memory for low energy
Break the Vmin barrier
FPU, logic & latches
Register Files,
SRAM
2. Coping with variations due to NTV
Freq degradation
Variation in performance
Functionality loss
5. Hierarchical, heterogeneous IC
Busses
X Bars
Circuit & Packet Switched
4. Instrumentation for introspection
Energy measurement
Performance feedback
Ambient conditions
3. Fine grain power management
Voltage Regulator
Buck or Switched Cap
Power gating
Frequency control
6. Overhaul memory subsystem

## Slide 8: Exascale SW Challenges
1. Extreme parallelism O(billion)
Programming model
Data locality
Legacy compatibility
2. Programming model & system
Data flow inspired
Gentle slope programming
(Productivity to high performance)
3. New execution model
Event driven
Asynchronous
Dynamic scheduling
Runtime system
5. Challenge applications
New algorithms
Locality friendly
Immunity to tapered BW
4. Self awareness
Observation based
Monitor, continuously adapt
Objective function based runtime optimization
6. System level resiliency research

## Slide 9: Exascale SoC Processor Straw-man
I$
D$ (64KB)
RF
FPMAC
Dec
Simple Core
Large shared Cache/Mem
Core
Large shared Cache/Mem
Block
Large shared Cache/Mem
Cluster
SoC Targets (5 nm) |  | 
Die Size | mm | ~25
Frequency | GHz | >2
Cores |  | ~4096
FP Perf | Tera-Flops | >16
Power | Watts | < 100
Energy Efficiency | pJ/FLOP | 4-6
 | GF/Watt | > 200
Mem Controller
IO (PCIe)
Interconnect Fabric
Interconnect Fabric
SoC

## Slide 10: Node
SoC
......
LPDDR
LPDDR
3D
LPDDR
LPDDR
3D
......
~1 TB
1 TB/s
Total BW
High performance, low power
DDRx
DDRx
DDRx
DDRx
......
4 TB
High capacity, low cost
Processor Node
......
IC Fabric

## Slide 11: Interconnect Switch Straw-man
Data Buffer
Data Buffer
Data Buffer
Data Buffer
Data Buffer
Data Buffer
Data Buffer
Data Buffer
Arbitration Logic
Arbitration Logic
Arbitration Logic
Arbitration Logic
Switching Fabric
Optical PHY
Optical PHY
Optical PHY
Optical PHY
Electrical PHY
Electrical PHY
Electrical PHY
Electrical PHY
Electrical PHY
Electrical PHY
Electrical PHY
Electrical PHY
Local Electrical Switch Network

## Slide 12: On-die Data Movement vs Compute
Interconnect energy (per mm) reduces slower than compute
On-die data movement energy will start to dominate
Chart: Technology (nm)
| 90 | 65 | 45 | 32 | 22 | 14 | 10 | 7
Comp (Rel) | 1 | 0.56711 | 0.34452 | 0.22108 | 0.14965 | 0.10669 | 0.077637 | 0.057069
IC (Rel) | 1 | 0.74288 | 0.59099 | 0.49647 | 0.43977 | 0.41016 | 0.3903 | 0.37503
On die IC energy/mm
Compute energy
6X
60%
Notes: Having looked at energy efficiency of the compute, let’s now focus on the communication aspects.
The graph to the left compares energy per operation of a compute operation over successive generation of technologies, and compares against energy of moving a bit over on-die interconnect by say one mm.
Notice that the interconnect energy reduces much slower than the compute energy. Therefore, interconnect related energy will start dominating in the future designs, necessitating restricting data movement.
Off-die interconnect energy and bandwidth is shown to the right. The energy is reducing, and the bandwidth is increasing, but probably not at the rate desired to support compute.
Also notice that there is a big gap between what is reported in the research papers in terms of energy efficiency and bandwidth, vs what is actually realized in production.
We need to pay attention to both on-die as well as off-die communication much more than in the past.

## Slide 13: Interconnect vs Switch Energy
Chart: On-die interconnect length (mm)
| 1 | 5 | 10 | 15 | 20
ps | 300 | 1500 | 3000 | 4500 | 6000
pJ/bit | 0.04 | 0.2 | 0.4 | 0.6 | 0.8
Switch delay
Switch energy
Switch energy
With scaling
Repeated wire delay
Wire energy

## Slide 14: Interconnect Structures
Buses over short distance
Shared bus
1 to 10 fJ/bit
0 to 5mm
Limited scalability
Multi-ported Memory
Shared memory
10 to 100 fJ/bit
1 to 5mm
Limited scalability
X-Bar
Cross Bar Switch
0.1 to 1pJ/bit
2 to 10mm
Moderate scalability
1 to 3pJ/bit
>5 mm, scalable
Packet Switched Network
Board
Cabinet
System
Hierarchy & Heterogeneity

## Slide 15: Exascale HW System

## Slide 16: Bandwidth Tapering
Chart: Byte/FLOP
| Core | L1 | L2 | Chip | Board | Cab | L1Sys | L2Sys
B/Flop | 24 | 6 | 1.5 | 0.375 | 0.09375 | 0.023438 | 0.0058594 | 0.0014648
B/Flop Tapered | 24 | 6.6524 | 1.1257 | 0.19047 | 0.026473 | 0.0044796 | 0.00046795 | 4.8884e-05
Intelligent BW tapering is necessary
Naïve, 4X
Severe

## Slide 17: NTV Operation for Energy Efficiency
Leakage power dominates
10X increase in Energy Efficiency
Variations become worse
Die to die frequency
Across temperature
H. Kaul et al, 16.6: A 320mV 56μW 411GOPS/Watt Ultra-Low-Voltage Motion-Estimation Accelerator in 65nm CMOS ISSCC 2008
H. Kaul et al, “Near-Threshold Voltage (NTV) Design—Opportunities and Challenges”, DAC, 2012

## Slide 18: NTV Design Considerations (1)
Conventional dual-ended write RF cell
NTV friendly, dual-ended transmission gate RF cell
NTV friendly Flip-Flop
NTV friendly Vector Flip-Flop
H. Kaul et al, “Near-Threshold Voltage (NTV) Design—Opportunities and Challenges”, DAC, 2012

## Slide 19: NTV Design Considerations (2)
NTV friendly multiplexer
Two-stage, cascaded split-output level shifter
Ultra-low voltage, split-output level shifter

## Slide 20: Integration of IP Blocks
Clock
Enable
Power Enable
Power Enable#
Synthesizing clock gating
Synthesizing power gating
Integrated
Voltage
Regulator
&
Control
Vdd
L
Vout
Integrated voltage regulators
Enable DVFS and NTV operation
Other traditional IP blocks:
Accelerators, Memory controller, PCIe, …etc.

## Slide 21: Choice of Technology
C.-H. Jan et al, “A 22nm SoC Platform Technology Featuring 3-D Tri-Gate and High-k/Metal Gate, Optimized for Ultra-Low-Power, High-Performance and High-Density SoC Applications”, IEDM 2012
Chart: 
| HP | Std | LP | ULP
Freq (Relative) | 1 | 0.65741 | 0.37963 | 0.32407
Chart: SD Leakage Power (Relative)
| HP | Std | LP | ULP
Lkg Power (Relative) | 1 | 0.01 | 0.0003 | 0.00015
30% drop
100X drop
22 nm SoC Technology

## Slide 22: SoC Design Challenges
Challenge | Potential Solutions
1,000’s or cores Large die WD & DD Variations | Variation tolerance Dynamic, system level adaptation
Voltage scaling to NTV | New standard cell library?
Data movement dominates | Interconnect optimization
Multi-ported, various sizes of RF and memories | Memory and RF compilers
Integration of custom and off-the-shelf IP blocks | Soft IP, not hard IP
Complexity | Formal verification
Silicon cost | Architectural simplicity
Design for system efficiency | System level optimization tools
Process technology | HP vs LP—judicious choice